## Slide 1: FA-0399640
Failure Analysis Report

## Slide 2: Part inspection summary
N9K-C93108TC-EX SN: FDO22441MNA Service Request: 686997516 RMA: 800239238 Customer Request: No
Customer Problem: IQS2.0 PID Profile for N9K-C93108TC-EX=,

## Slide 3: Case review summary​
N9K-C93108TC-EX
SN: FDO22441MNA
The unit was received on our site, and I do not present physical damage.
Fault duplication: Yes​
The reported issue was duplicated, the UUT did not boot up

## Slide 4
Fault isolation: Yes
1.- Power on unit reboots multiple times.
Result: Fail. The unit has an issue related with the power sequence
2.- Check the IOFPGA image with a golden units.
Result: Fail. The enable of the power sequence was not generated for the FPGA this caused that the UUT did not boot.
4.- .Reflow IOFPGA
Result: Fail. The fault still exist
5.- Replaced IOFPGA
Result: Pass. Issue was solved
3.- Replace the IOFPGA image with a golden units.
Result: Fail. Same as before, can not enter loader

## Slide 5
The customer problem was caused by a hardware issue. The affected component information it shows below.
RefDes Location: FPGA(IO)
Part Number:16-4243-01
MPN: EP4CGX50CF23C8N
Vender: INTEL
DC: 1813
L/D: NAAAF56482
Conclusion